## Slide 1: Bonolo Masima: Supervisor Meeting 3
Thurs 2 July 2026 15:30 – Rankine

## Slide 2: Causal Inference for Robotic Grasp Failure Diagnosis under Perceptual Degradation
Simulation Pipeline
Data Collection
Structural Causal Model
Phase 1
MuJoCo scene • Contact-GraspNet IK controller • 432-trial experiment
COMPLETE
COMPLETE
Factorial grid (4×4×3×3×3) 432 trials • CSV logged
LLM Baseline
Fit SCM on collected data Counterfactual diagnosis
Zero-shot GPT-4o prompting Comparison with SCM accuracy
In progress
UPCOMING
Phase 2
Phase 3
Phase 4

## Slide 3: Scene in Mujoco

## Slide 4: GraspNet Pipeline
1. Render Depth
MuJoCo camera captures depth from controlled viewpoint (φ, θ)
→
2. Perturb Perception
Add depth noise σ_d Downsample to ρ% → degraded point cloud C_pc
→
3. Propose Grasps (CGN)
Contact-GraspNet returns N poses with confidence scores q_grasp
→
4. Execute via IK
Best pose → DLS Jacobian IK → arm moves to grasp position
→

## Slide 5: Poses in Contact Grasp Net

## Slide 6: Confidence Scores

## Slide 7: GRASP demo

## Slide 8: Results: 432 trials
σ_d (noise)
Mean n_grasps
Mean q_grasp
Mean e_pose
Success rate
0.000 (clean)
34.2
0.242
5.0 cm
71 %
0.005 (mild)
24.3
0.243
7.6 cm
43 %
0.020 (heavy)
3.2
0.202
11.1 cm
11 %
0.040 (severe)
0.1
0.163
17.5 cm
0 %
71 % success in clean conditions
Contact-GraspNet works well with full perception
43 % with mild noise (σ=0.005)
Early degradation already halves performance
0 % at σ_d = 0.040
Severe noise → zero valid grasps → guaranteed failure
n_grasps drops 340x from clean to severe noise. e_pose grows 3.5x. Both reflect the same causal root.
Success rate by noise level:
σ_d=0
71 %
σ_d=0.005
43 %
σ_d=0.02
11 %
σ_d=0.04
0 %

## Slide 9: Thank You!
#UofGWorldChangers
@UofGlasgow