## Slide 1
Causal Inference for Robotic Grasp Failure Diagnosis under Perceptual Degradation
Supervisor Meeting 3 · Thursday 2 July 2026
Bonolo Masima
MSc Robotics & AI · University of Glasgow
Research Question: Can a Structural Causal Model diagnose the root cause of a perception-induced grasp failure more accurately than a zero-shot LLM?

## Slide 2
Project Overview: Four-Phase Roadmap
Bonolo Masima · MSc Robotics & AI · University of Glasgow · Jul 2026
Phase 1
Simulation Pipeline
COMPLETE
MuJoCo scene • Contact-GraspNet IK controller • 432-trial experiment
Phase 2
Data Collection
COMPLETE
Factorial grid (4×4×3×3×3) 432 trials • CSV logged
Phase 3
Structural Causal Model
IN PROGRESS
Fit SCM on collected data Counterfactual diagnosis
Phase 4
LLM Baseline
UPCOMING
Zero-shot GPT-4o prompting Comparison with SCM accuracy

## Slide 3
Phase 1: The Simulation Pipeline
How perception drives grasping
Bonolo Masima · MSc Robotics & AI · University of Glasgow · Jul 2026
1. Render Depth
MuJoCo camera captures RGBD from controlled viewpoint (φ, θ)
→
2. Perturb Perception
Add depth noise σ_d Downsample to ρ% → degraded point cloud C_pc
→
3. Propose Grasps (CGN)
Contact-GraspNet returns N poses with confidence scores q_grasp
→
4. Execute via IK
Best pose → DLS Jacobian IK → arm moves to grasp position
→
5. Log Outcome
Proximity check: e_pose < 6.5 cm? → Y = 1 (success) or Y = 0 (fail)
Key insight: every component of this pipeline is parameterised by the exogenous variables — degrading perception cascades to grasp failure.

## Slide 4
The Causal Variables
What we measure and why
Bonolo Masima · MSc Robotics & AI · University of Glasgow · Jul 2026
Variable
Role
What it measures
Why it matters
σ_d
Exogenous
Gaussian noise added to depth buffer
Controls sensor degradation — root cause 1
ρ
Exogenous
Fraction of point cloud retained
Controls observation sparsity — root cause 2
φ, θ
Exogenous
Camera elevation & azimuth
Controls geometric visibility of the object
C_pc
Intermediate
Object pixels visible in image
Perception quality — first downstream effect
q_grasp
Intermediate
CGN confidence score (force-closure quality)
Key proxy: how reliable is the proposed grasp?
e_pose
Intermediate
Euclidean error: proposed vs true position
Accuracy of grasp localisation
n_grasps
Intermediate
Number of valid grasp candidates
Richness of the CGN output
Y
Outcome
Binary success (e_pose < 6.5 cm)
Did the system correctly locate the object?
Confidence score q_grasp is the natural causal mediator: it collapses perception quality into a single actionable signal for the SCM.

## Slide 5
Results: 432-Trial Factorial Experiment
Clear monotonic causal degradation
Bonolo Masima · MSc Robotics & AI · University of Glasgow · Jul 2026
σ_d (noise)
Mean n_grasps
Mean q_grasp
Mean e_pose
Success rate
0.000 (clean)
34.2
0.242
5.0 cm
71 %
0.005 (mild)
24.3
0.243
7.6 cm
43 %
0.020 (heavy)
3.2
0.202
11.1 cm
11 %
0.040 (severe)
0.1
0.163
17.5 cm
0 %
71 % success in clean conditions
Contact-GraspNet works well with full perception
43 % with mild noise (σ=0.005)
Early degradation already halves performance
0 % at σ_d = 0.040
Severe noise → zero valid grasps → guaranteed failure
n_grasps drops 340x from clean to severe noise. e_pose grows 3.5x. Both reflect the same causal root.
Success rate by noise level:
σ_d=0
71 %
σ_d=0.005
43 %
σ_d=0.02
11 %
σ_d=0.04
0 %

## Slide 6
Why Use q_grasp (Confidence Score)?
Defending the key intermediate variable
Bonolo Masima · MSc Robotics & AI · University of Glasgow · Jul 2026
What is q_grasp?
• Learned force-closure quality score from Contact-GraspNet
• Trained on 17 million simulated grasps across diverse objects
• Outputs a score in [0, 1] — higher = more likely successful grasp
• Encodes: finger alignment, approach direction, contact geometry
• Not a hand-crafted heuristic — learnt from data
Why it fits the SCM
• Collapses complex perception quality into one scalar — ideal SCM node
• q_grasp responds monotonically to perception degradation (σ_d↑ → q↓)
• Clean: q_grasp = 0.242 avg, 34 candidates
• Noisy (σ_d=0.04): q_grasp = 0.163, < 1 candidate on average
• Satisfies the SCM Markov condition: q_grasp screens off σ_d from Y
• Can be used in logistic outcome equation: P(Y=1) = σ(λq_grasp + ...)
SCM outcome eq: Y = f(q_grasp, e_pose, n_grasps, ε) ← q_grasp is the natural summary of perception quality

## Slide 7
Current Limitations & Future Improvements
Bonolo Masima · MSc Robotics & AI · University of Glasgow · Jul 2026
Current Limitations
Physical lift not achieved
Gripper geometry (primitive capsules) + position-only IK ignores CGN orientation. Fingers approach top-down and miss the cylinder equator.
Proximity criterion as proxy
Success = e_pose < 6.5 cm (not actual lift). Scientifically defensible for causal analysis, but a real lift would strengthen the thesis.
Single object type
Only a cylinder tested. Different shapes may change CGN behaviour and should be explored in future work.
Future Improvements
6-DoF IK + full CGN orientation
Use the full 4×4 pose matrix from CGN (approach & closing directions) to align the gripper correctly → enables real physical lift
Real Panda mesh assets
Switch from primitive capsules to mujoco_menagerie Panda (or robot_descriptions package) for realistic contact geometry
SCM counterfactual interventions
Do(σ_d = 0) on a failed trial → did adding noise cause failure? This is the core causal diagnosis comparison with the LLM
LLM baseline (Phase 4)
Give GPT-4o the observable variables (C_pc, q_grasp, e_pose, n_grasps, Y) and ask it to identify the root cause — no access to σ_d or ρ

## Slide 8
Next Steps & Timeline
Bonolo Masima · MSc Robotics & AI · University of Glasgow · Jul 2026
Week 1 (now)
Fit SCM
Structural equations via OLS on intermediates; logistic regression on Y
Week 2
Counterfactual Diagnosis
Pearl 3-step procedure on held-out failed trials — SCM root cause
Week 3
LLM Baseline
Zero-shot GPT-4o on same failures; compare diagnosis accuracy vs SCM
Week 4
Results & Discussion
Tables, Figs, robustness checks; begin writing Chapter 4 & 5
Week 5
Full Draft to Supervisor
Complete dissertation draft submitted for feedback
Target dissertation submission: mid-August 2026 | Causal analysis complete by end of Week 4